## Slide 1: Stryke Force Talon SRX Motor Training Course
December 9, 2017
Jerry Culp

## Slide 2: Agenda
How does a motor work (turning current into rotary motion)
Motor performance (speed/torque curves and what they mean)
Talon SRX overview
Talon control modes
Encoders
Configuring an entire axis (Talon SRX + sensor + motor)
  Open loop
  Closed loop - PID
  Tuning a Closed loop
    Velocity
    Position
    Motion Magic

## Slide 3: How does a motor work
The Right Hand Rule

## Slide 4: How does a motor work

## Slide 5: How does a motor work

## Slide 6: How does a motor work

## Slide 7: How does a motor work

## Slide 8: How does a motor work

## Slide 9: How does a motor work

## Slide 10: How does a motor work
This is how we make torque

## Slide 11: How does a generator work
What is “Back EMF”?

## Slide 12: How does a motor work
Electrical Schematic of a Motor
Amps = Torque
Volts = Speed

## Slide 13: Motor Performance
Chart: 
| 0 | 5330
12 | 2.41 | 0
Stall Torque
Free Speed

## Slide 14: Motor Performance
Chart: 
| 0 | 444.16666666666669
1 | 0.20083 | 0
2 | 0.40167 | 0
3 | 0.6025 | 0
4 | 0.80333 | 0
5 | 1.0042 | 0
6 | 1.205 | 0
7 | 1.4058 | 0
8 | 1.6067 | 0
9 | 1.8075 | 0
10 | 2.0083 | 0
11 | 2.2092 | 0
12 | 2.41 | 0

## Slide 15: Motor Performance
Speed Torque Curve

## Slide 16: Motor Performance
CIM
Lots of copper
Low speed
Heavy
No fan
Bag
Less copper
Medium speed
Light
No fan
775
Less copper
High speed
Light
Fan

## Slide 17: Motor Performance - CIM

## Slide 18: Motor Performance - 775

## Slide 19: Motor Performance
Motor | Price | Max Power | Free Speed | Stall Torque | Weight
CIM | $28 | 337 W | 5,310 rpm | 2.4 N-m | 2.82 lbs
Mini-CIM | $25 | 230 W | 6,200 rpm | 1.4 N-m | 2.16 lbs
BAG | $25 | 147 W | 13,100 rpm | .43 N-m | .71 lb
RS-775pro | $18 | 347 W | 18,700 rpm | .71 N-m | .74 lb
RS-550 | $7 | 253 W | 19,300 rpm | .48 N-m | .48 lb
AM-9015 | $14 | 179 W | 16,000 rpm | .43 N-m | .5 lb
Snow Blower Motor | $39 | 20 W | 100 rpm | 7.9 N-m | 1.1 lbs

## Slide 20: Motor Performance
Gearbox Options (change the speed / torque relationship)

## Slide 21: Motor Performance
Heat!

## Slide 22: Motor Performance - PWM
= 6 volts
= 9 volts
= 3 volts
ON = 12 volts OFF = 0 volts
Pulse Width Modulation

## Slide 23: Motor Performance - PWM

## Slide 24: Talon SRX

## Slide 25: Talon SRX Wiring

## Slide 26: Talon SRX Communications
PWM
CAN Bus
  Frames
    Command – 10mS
    General – 20mS
    Feedback – 20mS
    Quadrature – 100mS
    Analog – 100mS
Frame rates are programable
Watch out for CAN bus overload

## Slide 27: Talon SRX Blink Codes

## Slide 28: Talon SRX Versions
Hardware
  1.4 3.3 vs 5.0 volt Quadrature pins (Qb & Qi are limited to 3.3)
  1.7
Firmware
  X.XX (2018)
    Remote sensor CAN connectivity
    4 PID slots
  2.34 (2017)
  2.00 (2016)
  older

## Slide 29: Talon SRX Control Modes
Duty Cycle (-1 to 0 to +1)
Voltage (-12 to 0 to +12)
Velocity
Position
Current Control
Slave
Motion Control
Motion Magic

## Slide 30: Control – Velocity Mode
The Talon will vary the drive voltage to move the motor torque (current) up and down on the red line to maintain a fixed speed. The Back EMF (VG) of the motor will always match the speed. The Talon drive voltage beyond the BEMF is used to drive more current through the motor’s winding resistance (Ra) to generate more torque.

## Slide 31: Talon SRX Parameters
P
I
D
FF
Izone
Max voltage out (+&-)
Nominal voltage (+&-)
Min Acceptable Error
Voltage Ramp
Voltage Ramp Closed loop
Current limit
Hard limits
  NO / NC
Soft limits
  Value
Reverse Encoder
Reverse Output
Encoder Scaling
Velocity Filtering

## Slide 32: Talon SRX Sensors
Quadrature Encoder
  US Digital
  CIMcoder
  AM Mag
  CTR magcoder
Analog Encoder
  Rotary potentiometer
  String potentiometer
Limit Switch
  Forward
  Reverse
  Soft limits
Other
  DC Voltage
  Frequency
  Period
  Duty Cycle

## Slide 33: Encoders - Quadrature
How do they work?

## Slide 34: Encoders - Quadrature

## Slide 35: Encoders - Quadrature
CIMcoder
  Magnetic
  20 cycles per rev
  80 counts per rev

## Slide 36: Encoders - Quadrature
CTR Magcoder
  Magnetic
  1024 cycles per rev
  4096 counts per rev
  Includes Absolute!

## Slide 37: Encoders - Quadrature
US Digital E4T
  Optical
  360 cycles per rev
  1440 counts per rev

## Slide 38: Encoders - Quadrature
Andy Mark
  Magnetic
  7 cycles per rev
  28 counts per rev

## Slide 39: Encoders – Rotary Pots
Several Manufactures
  Analog
  Need an ATD
  Absolute

## Slide 40: Encoders – String Pots
Several Manufactures
  Analog
  Need an ATD
  Absolute

## Slide 41: Encoders – Sentinel Interface
Shameless plug … $18 and in stock at Andy Mark!
The Sentinel puts an end to any and all interface issues

## Slide 42: Control
Open Loop
  Fixed voltage – Speed changes with load
    Duty Cycle (-1 to 0 to +1)
    Voltage (-12 to 0 to +12)
Closed Loop (add an encoder)
  Variable voltage – Speed stays constant with load
    Speed
  Variable voltage – Position stays constant with load
    Position & Motion Magic
  Variable voltage – Torque stays constant with load (somewhat)
    Constant Current

## Slide 43: Control – PID
What on earth is PID?
Motor & Encoder
Encoder wires
Motor power
Output shaft

## Slide 44: Control – P
Lets start with P

## Slide 45: Control – Velocity Mode
The Talon will vary the drive voltage to move the motor torque (current) up and down on the red line to maintain a fixed speed. The Back EMF (VG) of the motor will always match the speed. The Talon drive voltage beyond the BEMF is used to drive more current through the motor’s winding resistance (Ra) to generate more torque.

## Slide 46: Control – P only
Walk the line … a real live control loop!

## Slide 47: Control – Tuning
You can tune a piano, but you can’t tuna a fish

## Slide 48: Control – PI
Add in I

## Slide 49: Control – PID
Add in D

## Slide 50: Control – PID with FF
Feed Forward
Fterm= Kf(t)

## Slide 51: Control – PID Effects

## Slide 52: Control – The Real Thing
Lets do some tuning!

## Slide 53: Tuning - Velocity
CIM & CIMcoder with a Pulley (no load)
  I limit
  F
  P
  I
  Izone
  D
  Velocity Filter
  Voltage Ramp

## Slide 54: Tuning - Velocity
Velocity Filter – Period
Velocity Filter - Samples
Chart: Talon Velocity Filter
Chart: Talon Velocity Filter
Period – 100mS
Samples - 64
Period – 25mS
Samples - 8
Shaft
Talon input
After Period
After Samples
Talon counts
Talon counts

## Slide 55: Tuning - Velocity
CIM & CIMcoder with a Pulley (no load)
with Drag
with Inertia
with Drag and Inertia

## Slide 56: Tuning - Position
9015 with Vex 100:1
  I limit
  P
  D
  Voltage Ramp
  Voltage Max Limit

## Slide 57: Tuning – Motion Magic
A Position loop running on top of a Velocity loop
  I limit
  F
  Cruise
  Acceleration
  P
  D
  Nominal Error (min acceptable error)

## Slide 58: Quick Guide to Simple Tuning
Disclaimer!
  This is a quick start on how to get something up and running with a “seat of the pants” approach.
  This is not a comprehensive tuning process.

## Slide 59: Quick Guide to Simple Tuning
For a standard velocity loop with some amount of static load / drag
  Ensure FF, P, I, D, Izone are all set to zero. Ensure Max FWD and Max REV volt are set to 12 and -12.
  Ensure your encoder is in phase with your motor. Run the motor in voltage mode and note that a positive voltage creates a positive velocity. If not, reverse the encoder.
  Select Velocity mode
  Increase FF until the actual velocity (process variable) is close to, but not higher than the requested velocity (set point) throughout the desired dynamic range.
  Increase P until the loop goes unstable indicated by continual oscillations or a long time to stop oscillating. Then cut that P value in half. Check it throughout the entire dynamic range.
  Run through the range of desired set points and note the largest error at any single speed.
  Set Izone to 1.5x of the largest error observed in step 6
  Increase I until the loop goes unstable. Reduce I until the settling time is optimized. You will end up trading off some overshoot vs a longer settling time. (I will likely be one tenth of P)
  If required, increase D to reduce the overshoot incurred in step 8. (D will likely be 10 to 100x of P)
  Go back and adjust P, then I, then D to observe the effects. They all interact so after the first pass, there may be some tweaks that will improve the performance.
  You may find that limiting the Max FWD and Max REV will help stabilize the loop if you don’t need the full speed.

## Slide 60: Quick Guide to Simple Tuning
For a standard position loop with some amount of static load
  Ensure FF, P, I, D, Izone are all set to zero. Ensure Max FWD and Max REV volt are set to 12 and -12.
  Ensure your encoder is in phase with your motor. Run the motor in voltage mode and note that a positive voltage creates a positive position change. If not, reverse the encoder.
  Select positon mode
  IF there is a static load on the axis that ALWAYS loads the system in the SAME direction, Increase FF until position (process variable) is close to, but not higher than the requested position (set point) throughout the desired dynamic range. If there is no static load leave FF at zero.
  Increase P until the loop goes unstable. It will continue to oscillate or takes a long time to settle. Then cut that P value in half. Check it throughout the entire dynamic range.
  Increase D to manage the position overshoot that results from increasing P. With some D, you will likely be able to increase P beyond what was stable with P alone.
  A PD approach may be sufficient to drive the position close enough to the desired setpoint.
  You may find that limiting the Max FWD and Max REV will help stabilize the loop if you don’t need the full speed.
  If you need more precision … continue

## Slide 61: Quick Guide to Simple Tuning
For a standard position loop with some amount of static load (continued)
  Run through the range of desired set points and note the largest error at any position.
  Set Izone to 1.5x of the largest error observed in step 3
  Increase I until the loop goes unstable. Reduce I until the settling time is optimized. You will end up trading off some overshoot vs a longer settling time.
  Go back and adjust P, then I, then D to observe the effects. They all interact so after the first pass, there may be some tweaks that will improve the performance.
  If you have a high resolution encoder (lots of ticks per distance) you may find the increasing the Minimum Error to the max you can tolerate will help stabilize the loop.
  You may also find that increasing the nominal FWD and REV voltages to the minimum amount that will actually make the axis move (in voltage mode) will also help stabilize the loop, especially if you are using some I.
  If your axis goes over center where gravity or some other force loads the system in both directions, do no use any FF. Just start with P and go from there.

## Slide 62: REO Speedwagon 1978
You can Tune a piano, but you can’t Tuna a fish

## Slide 63
Questions?